## Slide 1: Renewable Energy & Solar Update Hythe Environment Group March 19th 2018 Matthew Morris Independent energy & sustainability consultant

## Slide 2: Solar Energy
Part 1:
  Renewable energy update
  Update on FiT and uptake of solar PV
  The end of subsidies - where is renewables policy heading
Part 2:
  Technology and performance - general update
  Rough guide to sizing and costing
  How to buy and group purchasing
  Have we forgotten solar thermal?

## Slide 3: Energy Transition in Europe
Power:
  Huge shift from coal to gas
    3-5% of UK gas demand from LNG
  Dependency on coal declining
  Power consumption growth also slowing
  Contribution from renewables now significant
  But, electricity interconnectors keep grid secure
Heat:
  Large scale geothermal becoming viable
  Biomass CHP important for some countries
  UK renewable heat mainly stimulated by subsidies
    Biomass, solar thermal, heat pumps
  Biogas (biomethane)
    550 AD plants / 100 grid-injection plants

## Slide 4: UK Energy Demand

## Slide 5: UK Energy Mix: Low carbon electricity

## Slide 6: UK Energy Mix: Electricity generation

## Slide 7: UK Energy Mix: Monthly electricity generation

## Slide 8: UK Energy Mix: Decline of coal

## Slide 9: UK Energy Mix: CO2 emissions

## Slide 10: UK Government Energy Policy
Critically Important in developing renewable RE projects
  From 2002: The Renewables Obligation drove investment in large-scale projects
  Since 2010: FiT for medium-scale
  Since 2011: RHI for heat projects
UK solar market now mature - costs continue to decline
The Government is starting to exit from small-scale subsidies
CM and CfD now driving investment in large-scale projects
Some projects are now subsidy free

## Slide 15: Demand Response
Rapid response to changes in grid frequency
  Helps balance grid to 50Hz
  Important for avoiding blackouts during peak demand
Only since early 2000s
  STOR: ‘turndown’ – large users turn things off
  FFR: Rapid power generation
  FCDM: Interruption of demand customers
  EFR: Sub-second power supply for limited duration
Firm Frequency Response (FFR):
  10-30 seconds
  Usually gas, oil and diesel ‘peaking’ plants
Enhanced Frequency Response (EFR):
  Sub-second response
  First auction in 2016
  8 battery storage bids successful
  £/MW far below £20/MW bid price
  Sector needs new auctions to be viable into future
Plus imports and exports via Interconnectors
All of the above add up to the UK’s ‘capacity margin’ and are part of the UKs Electricity Market Reform
http://www.dynamicdemand.co.uk/grid.htm#

## Slide 16: Latest Capacity Market Auction: Feb 2018
Another big shift away from coal
What is filling the gaps:
  Existing gas & nuclear
  New interconnectors
  Decentralised energy
UK power system is both more localised and more international
Decreasing dependence on large-scale power generation
But…
  Gas, coal and DSR dominated latest auction
  Very little solar and battery storage
  Specific support for renewables is starting to disappear
Biggest challenge for security of supply now about providing flexibility rather than the overall level of capacity

## Slide 17: Latest Capacity Market Auction: Feb 2018

## Slide 20: Renewable Energy (RE)
Europe:
  90% of new power capacity in Europe in 2016 from renewable sources
  Mainly power technologies (wind, solar)
  European utilities moving massively into sustainable energy
  Wind and solar rapidly becoming cheapest source of energy
UK:
Significant increase in deployment since 2010
UK power generation 2016:
  9% coal (record low)
  21% nuclear
  25% renewables (record high)
  43% gas
EU policy has been the catalyst
National subsidies were the driver
Installation costs reducing

## Slide 21: UK Energy Production: Monday 4:20 pm

## Slide 22: Solar Energy
Part 1:
  Renewable energy update
  Update on FiT and uptake of solar PV
  The end of subsidies - where is renewables policy heading
Part 2:
  Technology and performance - general update
  Rough guide to sizing and costing
  How to buy and group purchasing
  Have we forgotten solar thermal?
  Future

## Slide 23: Technology & Performance
Solar PV
  No major breakthroughs
  Most panels are in the 15-17% range still
  >21% possible
  Mono better than poly
Main advantages from design and materials:
  Ultra-thin amorphous silicon layers reduce losses
  Surface structures internal materials capture more sunlight
  High Efficiency Performance at High Temperatures
Larger panels now available:
  300 wp more common
  Better for larger roofs
Warranties
  25 year product and performance warranty
  Linear performance guarantees (e.g. 90.76% after 25 years)

## Slide 24: Technology & Performance
Solar Panel Manufacturer | Minimum Efficiency (%) | Maximum Efficiency (%) | Average Efficiency (%)
SunPower | 19 | 22 | 21
Panasonic | 19 | 22 | 20
LG | 17 | 20 | 18
Heliene Inc. | 16 | 19 | 17
Solaria | 19 | 19 | 19
Itek Energy | 16 | 19 | 18
JinkoSolar | 16 | 19 | 17
Renogy Solar | 15 | 19 | 17
Silevo | 17 | 19 | 18
Silfab | 15 | 18 | 17
Mission Solar | 16 | 18 | 17
Hanwha Q CELLS | 16 | 18 | 17
CentroSolar | 15 | 18 | 16
Trina Solar Energy | 15 | 18 | 16
Canadian Solar | 16 | 18 | 17
Suniva Inc | 17 | 18 | 17
Grape Solar | 16 | 18 | 17
SolarWorld | 15 | 18 | 17
ET Solar | 15 | 18 | 17

## Slide 25: Technology & Performance
Potential Induced Degradation (PID)
  PID is a phenomenon which affects some PV modules with crystalline Si cells
  Causes gradual deterioration of performance
  30%+ after a few years
Increasing indications that many cell types display this failure pattern
Major influencing factors:
  Solar cells: Structure of the PV cells and anti-glare coatings
  PV module: Materials used in the PV module also play a role
  System configuration: Length of module strings, inverter type and earthing
  Time: PID not immediately apparent - months to a few years

## Slide 26: Technology & Performance
Detection:
  Data
  Analysis of trends and changes
Solutions:
  Replacing PID affected modules
  Replacing inverters
Buy high quality modules in the first place

## Slide 27: Technology & Performance
Light Induced Degradation (LID)
  Loss of performances arising in the very first hours of exposition to the sun
  LID related to the quality of the wafer manufacturing
  1-3% loss in PV effect
A set of ‘identical’ PV panels may therefore have different outputs
Higher quality manufacturers test for output and provide better warranties and guarantees
Low cost panels may be problematic

## Slide 28: Improved warranties
Linear performance warranties
  Majority of panels come with a 25-year performance guarantee
  E.g. guaranteed electrical production for 10 years at 90% of rated power output and 25 years at 80%.
  This is the standard model of degradation
Some manufacturers go further:
  E.g. 95% of rated power for the first 5 years
  declining by no more than 0.4% per year the following 20 years
  Therefore, guaranteed 87% of rated power output at 25 years

## Slide 29: PERC, Half Cut & HJT Cells
PERC:
  Passivated Emitter Rear Cell
  Improved module structure – absorbs more light
Half-Cut:
  Interconnects between cells can cause loss of power
  Cutting solar cells in half has been proven to be an effective way to lower resistive power loss
  Can potentially boost power output between 5-8 watts per module
Heterojunction (HJT) bi-facial cell (bifaciality):
  HJT cells fuse the best attributes from mono crystalline silicon cells (superior absorption) and amorphous silicon cells (excellent passivation) for a specialized cell that is immune to PID and LID

## Slide 30: PV array cleaning
Contaminants will build up over time
  Airborne dust particles
  Sticky tree and plant sap
  Lichen
  Soot
  Bird droppings
Some locations worse than other
Panel pitch important factor
Accumulation creates shading
Shading = financial loss
But cleaning panels costs money
Decision to clean based on cost-benefit analysis
Use data to detect trends
Inspect for damage
Self-clean if safe to do so

## Slide 31: Shading
Shading can have a big impact on output (up to 50%)
One shaded cell can affect performance of a panel and string
Embedded diodes in panel help reduce shading losses
Hot spot damage: Cells can be damaged by overheating caused by shading
Solutions:
  Don’t install on a badly shaded roof
  If shaded opt for a smaller array
  Break the array into smaller sections and use a correctly sized inverter on each section (with dual MPPT)
  Use micro-inverters (e.g. Tigo, SolarEdge)
Cut back vegetation that has grown since array was installed

## Slide 32: Inverters
Inverters convert DC from the array to AC for use within the home (and export to the grid)
They are constantly ‘on’ and manage variable power loads for long periods of time
Like most pieces of electrical equipment they have a lifespan and may fail without warning
Faults can be common and east to resolve:
  Blown fuses
  Tripped breakers
  Broken wires/ solder joints
Other faults are more serious and replacement is required

## Slide 33: Inverters
String Inverters:
  Lower initial cost
  Easier to install and maintain
But…
  String inverters treat a group of panels as if it were a single large panel
  Any problems with one panel are felt across the entire string e.g. shading
  Large inverters can take up space
Micro Inverters:
  Higher cost, but reducing
  More complex/ costly to install (1 per panel)
  Some are built-in
But…
  Micro inverters use power point tracking - array not affected by shading as badly
  Easier to fix - single point-of-failure
  Operate at a lower power point – electronics are simpler

## Slide 34: MPPT Inverters
Maximum Power Point Tracking
  Maximises power extraction under all light conditions
  Necessary because internal impedances vary throughout the course of the day (due to solar irradiance and cell temperature)
  The MPPT circuit constantly monitors the array voltage and current
    Attempts to drive the operating point of the inverter to the maximum power point of the array, resulting in the highest energy harvest
  Dual Vs single MPPT
    Depends on a number of array design factors
    Dual MPPT more flexible and potentially less expensive

## Slide 35: Micro Inverters
Often attached to rear of each panel
  Tracks MPPT of each module individually
  Allows more flexible installation design with multiple orientations, tilts and module types in the same string
  Mitigates shading impacts
  Reduces length of strings (cables)
  Sometimes referred to as DC optimisation
  Some micro-inverters included different levels of optimization (e.g. remote monitoring, alerts, shock protection, shutdown)
E.g. SolarEdge / Tigo

## Slide 36: Example Project

## Slide 37: Example Project
 | M3 | BeBa | Caplor | Invicta Clean Energy
Panel Make | Trina | JA Solar | Jinko | JA Solar
Panel model | TSM DD05A.05 | JAM6-K-SE-60-300-PR | JKM275PP-60(Plus) | JAM6(k)-60-Mono-280-300-PR
Efficiency (%) | TBC | 18.3 | 16.8 | 18.3
Tier 1 panel | Assumed Yes | Yes | Yes | Yes
Mono/Poly | Poly | Mono - with Black frame embedded if available at time of ordering | Poly | Mono
Qty panels | 94 | 94 | 94 | 94
Panel capacity (wp) | 300 | 300 | 275 | 300
Array size (kw) | 28.2 | 28.2 | 25.85 | 28.2
Dimension L (mm) | 1,650 | 1,650 | 1,650 | 1,650
Dimension W (mm) | 992 | 991 | 992 | 992
Dimension T (mm) | 35 | 40 | 40 | 35
Panel inclination (degrees) | 10 | 10 | 10 | 10 (n.b. 38 degrees is optimal, but need to take into account self-shading between rows and self-consumption to determine the recommended inclination)
DC optimisation | Yes - Solar Edge | Yes - Solar Edge | Yes - Solar Edge | Yes - Solar Edge
Qty DC optimisers | 47 | 94 (1 per panels embedded) | 47 | 94
Inverter | Solaredge SE25K - CCL | Solar Edge 25000 DC with inbuilt protection | Solar Edge 25000 | Solar Edge 25000
Qty inverters | 1 | 1 | 1 | 1
Inverter rating (kW) | 25 | 25 | 25 | 25
Surface protection | Rubber underlay | Rubber feet under the mounting frame are an option but NOT included | Console pods | AluGrid EDPM underlay
Mounting system | Schletter Alu Grid | K2 Mounting or Van de Valk Ballasted system decided after survey of rooftop | Aluminium mounting rails | Schletter Alu Grid

## Slide 38: Example Project
 | M3 | BeBa | Caplor | Invicta Clean Energy
Total ex. VAT | £32,690 | £31,597 | £33,193 | £31,200
Total inc. VAT | £39,228 | £37,916 | £39,831 | £37,440
Levelised cost (p/kwh) exc. VAT | £0.063 | £0.062 | £0.074 | £0.059
Levelised cost (p/kwh) inc. VAT | £0.076 | £0.075 | £0.088 | £0.071
Yr 1 ROI (%) | 12.4 | 17.9 | 13.7 | 17.4
Payback (years) | 7.3 | 8 | 7.3 | 5.7
Total FiT generation (Yr 1) | 1,180.0 | £1,115 | £1,016 | £1,147
Total FiT generation (20 yr) | £30,981 | £29,280 | 24,874 | 31,306
Total FiT export (Yr 1) | £687 | £681 | £605 | £695
Total FiT export (20 yr) | £18,054 | £17,874 | £14,824 | £18,972
Total savings (Yr 1) | £2,991 | £2,462 | £2,910 | £3,592
Total savings (20 yr) | £88,568 | £75,371 | £106,060 | £115,276
Total income and savings (Yr 1) | £4,858 | £4,258 | £4,530 | £5,434
Total income and savings (20 yr) | £140,604 | £122,524 | £141,760 | £165,553
Cost per kW | £1,159 | £1,120 | £1,284 | £1,106

## Slide 39: Other things to consider
Solar switches
  E.g. Immersun
  Diverts surplus solar power to water heating
  Excellent for reducing grid power usage
Batteries
  E.g. Telsa PowerWall 2, Nissan Futures
  Couple with PV array
  Charge during day – discharge at night (or charge EV overnight)
  Relatively expensive in UK (c. £5,000)

## Slide 40: Don’t forget solar thermal
Solar thermal
  Two main types:
  Flat plate or evacuated tube
Provides energy storage
C. 70% of hot water between May and Sept
Requires solar-specific tank
Usually just 2 panels for average house
Savings more modest due to low price of gas Vs electricity
  But very good if you only use electricity to heat water

## Slide 41: Solar Energy
Part 1:
  Renewable energy update
  Update on FiT and uptake of solar PV
  The end of subsidies - where is renewables policy heading
Part 2:
  Technology and performance - general update
  Rough guide to sizing and costing
  How to buy and group purchasing
  Have we forgotten solar thermal?
  Future

## Slide 42: Energy Production into the Future

## Slide 43: Energy Production into the Future

## Slide 44: Energy Production into the Future

## Slide 45: Energy Production into the Future

## Slide 46: Energy Production into the Future

## Slide 47: Non RE Alternatives